## Slide 1: Developing EPD’s For Aggregates
John J Yzenas Jr
john@jyc-consulting.net
jyzenas@nssga.org

## Slide 2: Agenda
What is a PCR / EPD?
Why does the Aggregate Industry need them?
  FHWA
  State Legislation
  Federal Legislation
  Paving Industry
Construction Aggregate PCR 2023
EPD Tool
  Site / Product Specific
  Availability
    Cost

## Slide 3: Product Category Rule (PCR)
​A PCR is a set of product category-specific requirements / rules / guidelines for developing life cycle assessment and reporting these findings in an Environmental Product Declaration for one or more product categories. Product category rules are reviewed and improved periodically over time (5-years).
Product Category Rule (PCR) development can be sponsored by a group of stakeholders, including associations, manufacturers, or other interested parties.
While PCRs must be prepared in accordance with the requirements set forth in ISO 14025, additional work may be needed to improve harmonization. PCRs for construction products must additionally comply with ISO 21930.
Copies of the ISO standards can be downloaded from ANSI: http://www.webstore.ansi.org.

## Slide 4: Environmental Product Declaration (EPD)
A verified report used to communicate the environmental impacts of a specific material (e.g., asphalt binder, portland cement) or product (e.g., asphalt mix, concrete mix).
EPDs promote more sustainable use of finite resources and create less stress on the environment.
EPDs are a life-cycle assessment developed by product manufacturers following the Product Category Rules (PCR) that are developed with industry stakeholders and LCA experts and subjected to a critical review process.
EPDs can be issued for a specific product from a specific producer but may also be issued for a generic product from a group of manufacturers (such as an association) that reflects the results of an industry-average LCA.
EPDs using the same product category rules can be compared to identify materials with improved environmental performance in terms of various environmental and resource use impacts (e.g., energy use, air pollution, global warming, ozone layer depletion).
https://www.fhwa.dot.gov/pavement/sustainability/pubs/hif19027.pdf

## Slide 5: Current Legislation
Year introduced | Source | Bill
2017 | California Legislature | Buy Clean California Act
2019 | Minnesota Legislature | HF 2204
2020 | New York State Senate | S542 (Original)
2021 | California Legislature | AB-1365, SB-778
2021 | Colorado State Assembly | HB 21-1303
2021 | Oregon State Legislature | HB 2688
2021 | New Jersey Assembly | AB 5223
2021 | Washington State Legislature | HB 1103
2021 | House of Representatives, 117th Congress | H.R.1512 CLEAN Future Act – Subtitle C – Federal Buy Clean Program
2022 | GSA | Inflation Reduction Act

## Slide 6: State / Federal Procurement Policy
Carbon Leadership Forum
Notes: DOT Projects

## Slide 7: FHWA: Sustainable Pavements Group
Actively Promoting the utilization of EPD’s
  Asphalt Pavement (NAPA)
  Cement (PCA)
    Slag Cement (SCA)
  Concrete Pavement (NRMCA)
  Construction Aggregates (NSSGA)
Developing best practice guidelines for PCR’s to facilitate harmonization.
FHWA LCA Development Program

## Slide 8: Asphalt LCA product system
FHWA

## Slide 9: PCR’s and ISO
ISO
International Standards
Organization

## Slide 10: Construction Aggregates PCR
Original –
  Program Operator: ASTM
  Adopted Jan. 2017
  Valid to Dec 2022 (extended)
Current –
  Program Operator: National Science Foundation (NSF)
Construction Aggregate, which can be defined as any combination of sand, gravel, crushed stone, crushed concrete, iron and/or steel slag sold to or used by the construction industry.

## Slide 11: Differences 2017 (Version 1) vs 2023 (Version 2)
The PCR has been renewed and updated to include conformance with ISO 21930 (2017).
Unbound asphalt is included in Version 2 of this PCR.
The title of the PCR has been modified to “PCR for Construction Aggregates”.
This PCR has been updated to include specific information on upstream data included in Annex A.
An underlying LCA has been completed to complement this PCR.

## Slide 12: Construction Aggregates?
Stone, sand and gravel – Crushed and/or processed
Slag aggregate
RAP aggregate (new)
Broken concrete aggregate (aka crushed concrete)

## Slide 13
Status of 2023 PCR
Committee started meeting May 2021
Draft completed 9/26/2022
Sent to expert review COB Oct 2022
Tech review comments received, response issued early Feb 2023
Public comment May 2023
PCR committee vote June 2023
Best guess…..Pending NSF Publishing
Current PCR expired 12/31/22 – NSF extension

## Slide 14: Committee / Reviewers

## Slide 15: Key Decisions
Scope A1 to A3
Basis
One English ton – 2000 lbs.
Conversion factors provided to metric
Weight is on an as-is (wet basis)

## Slide 16: Cutoff Boundaries

## Slide 17: Cut off Boundaries (Concrete and RAP)
7.1.6 – “All EDP related burdens from the initial RAP and broken concrete piles onward are accounted for in the aggregates PCR..”
7.2.5.2 -Slag allocation is economic

## Slide 18: Upstream Data
Annex A
Conforms to ACLCA Guidance for PCR
  aclca.org/pcr/
Specification of upstream data sources – publicly available*
First construction PCR to adopt ACLCA guidance on upstream data
Goal is quality data in EPD’s and to be consistent across construction materials

## Slide 19: Example – Upstream data

## Slide 20: Example – from Agg PCR Annex A

## Slide 21: Carbonation
Notes: Carbonation happens
Examined 100 year old concrete at the Colton site and found carbonation happens. Light layer is were this piece has carbonated.
Even after demolition. Concrete is crushed and still continues to carbonate.
Concrete is sucking it’s carbon dioxide back out of the air.

## Slide 22: Carbonation
Calculated carbonation benefits can be provided in EPD’s as part of “supplemental environmental information”. Not calculated as part of A1-A3.
Annex B
3 calculation methods
  1. apply factor of -0.35 kg CO2e/ton
  2. GCCA tool for Concrete and Cement V 3.1
  3. Quantify through field sampling and lab testing

## Slide 23: Issues

## Slide 24: Underlying LCA
A deep dive into construction aggregate environmental impacts…the highlight reel.

## Slide 25: Approximate Location Type of Participating Facilities

## Slide 26: Diesel, Electricity, and Explosives The Major GWP Contributors

## Slide 27: Operation Type

## Slide 28: Facts
Aggregates are low CO2e products. 3 to 8 kg/ton
How does this impact Concrete/Asphalt?
  Concrete EPD 300 kg CO2e/Yd. 1.5 tons aggregate = ~6 kg CO2e/Yd of concrete or 2%.
  Asphalt – Standard mix 50 kg CO2e/Ton. Agg at 0.95 ton agg/ton asphalt = ~4 kg CO2e/ton or 8%
    Substitute RAP and reduce GHG even further
  LCA commons value for Aggregate is 1.7 kg CO2e/ton
    Used by LCA practitioners
  Update LCA data - What is EPA going to do with all that money from the IRA???

## Slide 29: Transportation
Transportation of aggregate matters
  4 kg CO2e/ton to truck aggregate 15 miles
  0.8 kg/CO2e/ton by barge for same distance
How does this impact Aggregate EPD?
How does this impact asphalt, concrete EPD’s?
Keep in mind EPD’s are Cradle to Gate….

## Slide 30
Local Supplier
Remote Supplier
Ocean Transport

## Slide 31: Other PCR’s
Asphalt - Just completed. Will be Valid through 2027
Concrete PCR – Valid through Feb 22, 2024
Cement PCR - Valid through March 31, 2025
Aggregates PCR – Final ~ 2023

## Slide 32: The EPD Ecosystem
DOT
Database
Constr.
Mgmt
Software
Procurement Decisions
Aggregate EPDs
Concrete Mix EPDs
Asphalt Mix EPDs
Binder EPDs
Cement EPDs
3rd Party
Databases

## Slide 33: EPDs for Construction Aggregates
Coming soon:

## Slide 34: What is ?
Facility-specific EPDs
Preferential pricing for NSSGA Members
Streamlined data entry
Fast verification
Traditional and digital EPDs

## Slide 35: What you need to know and provide?
Plant type
Feedstock type or geology
Operation type (blasting, dredging, …)
Secondary processing/stockpiling locations
Grid energy use
Fuel use (diesel, natural gas, …)
Consumable inputs: flocculant, dust control

## Slide 36: Overall & Administrative Data
Data gathering period
Total Annual Production in short tons (not sales)
Operation type
Primary geology
Are your extraction and processing done in separate locations? That is, material is transported more than one mile by rail, truck or barge to processing? And finally, is the processing location treated as a separate area, with different tracking of electricitiy, fuel use, etc?
Do you have a secondary stockpile that tracks its electricity, water use, etc, separate from your main facility?
If you said yes to line 20 or line 21, what is the form(s) of transport and mileage between locations?
How many screens do you regularly have in use?
How many crushers do you regularly have in use?

## Slide 37: Inputs: Energy
Is your aggregate operation co-located with one or more other facilities (like an asphalt or concrete plant)? Do not include facilities that are leased, only those owned or operated by your quarry.
Do you have separate electrical metering for your aggregate facility?
If no, please enter your most informed estimate of the percent of electiricty used in the aggregate operation and your confidence in that estimate. Example: 75% electiricity used in aggegate ops, 60% confident in that estimate
Do you purchase renewable energy certificates or participate in an offsite renewable energy program? If so, please describe your REC or offsite renewables program.
Energy Source
Electricity, from Grid: kWh/yr
Electricity, from onsite solar: kWh/yr
Electricity, from onsite wind: kWh/yr

## Slide 38: Fuels (gallons / MCF)
Natural gas
Propane
Diesel
Gasoline
Recycled Fuel Oil
Residual Fuel Oil
Renewable Natural Gas (RNG)
Biodiesel
Biodiesel type (e.g. B20, B80, etc.)
Do you use any other fuels? List their types and quantity used here.

## Slide 39: Water (gallons / sq. ft.)
Water: Do you meter or otherwise track your water use? (if no, please use your best estimates for the following questions about water use)
Total water use
Water use for dust control
Water use for washing
Water source, well water
Water source, municipal water
Water source, ponds (including settling ponds)
Total surface area of ponds
What percent of your water is recycled?
If these water numbers are estimates, what is your confidence in your estimate?

## Slide 40: Other Consumables (lbs. / gallons)
Wear parts: Not all wear parts are needed for this calculation.
Provide just the following:
  Blasting agents (combine all types)
  Flocculants
  Dust control additives

## Slide 41: Recycled Concrete Aggregates (tpy)
Do you produce any recycled concrete aggregate (RCA)?
How many tons of RCA did you produce during the data gathering period?
How many tons of RCA did you receive during the period?
How many times did you receive RCA during the period?
How tall are your RCA stockpile(s)? If it changes often, give your best estimate for average height
On average, how old is your RCA stockpile?
Do you have a maximum target size for your RCA stockpile(s)?
Is your stockpile a typical cone shape, or do you manipulate it to another shape (e.g. spread out until X feet tall)
About what size is the RCA in your stockpiles?

## Slide 42: Production / End of Life
List the aggregates you produced & sold in your reporting year, in short tons.
Please add your products until you have accounted for all of your production / sales in your reporting year
How long has this quarry been in operation?
From the ranges given, about how long do you expect this quarry to continue to operate?
Do you have a quarry reclamation plan?
If so, what general category does it fit into?
(example) Landscaping boulders
(example) Cobbles
(example) 3/4"
(example) 1/2"
(example) 3/4" washed
(example) 1/2" washed
(example) Fine #2

## Slide 43: Sensitive information
All proprietary operational data is protected
Only final performance metrics are public
You choose which EPDs get published

## Slide 44: Workflow
Data collection
(excel)
Create Theta account
Define your facilities
Define your products
Create EPDs
Available today!

## Slide 45: Create an Account

## Slide 46: Define Facility

## Slide 47: Facility Data

## Slide 48: Products

## Slide 49: Timeline and What to Expect
Driven by PCR process: Soon
Register beta interest: underway
Beta testing: in process
Launch: when the PCR is published
Sign up for beta testing at
www.AggregateEpd.com

## Slide 50: Thank You! Questions?
Contributors:
John Yzenas Matt Hinck Ben Ciavola
jyzenas@nssga.org mhinck@calportland.com ben@wapsustainability.com